FW-190 A (big)

Kit of radio controlled electro-flyer

Wingspan:	1100 mm

Length:	960 mm

Flight weight:	400-550 g

The kit of this aircraft is mainly produced of extruded polypropylene EPP. This material ensures excellent durability and lifetime. Thanks its properties, this model enables pleasant flying and also more demanding acrobatic manoeuvres, perhaps even air fights.

Thanks the material, this model can survive many of collisions without damage and in any case, smaller damage can be repaired directly on the runway.

Model is to a great extent in good degree of completion and its completion will not require much time. Model is not designated for the beginners - that is why the assembly operation is not described in details. Design and final appearance of this model shall be modified considering selected engine and modeller’s skills and habits.

List of Kit parts:

Fuselage - EPP	3 pcs

Cabin - transparent	1 pc

Cabin frame	1 pcs

Wing - EPP	2 pcs

Control surfaces - EPP	2 pcs

Elevator joiner 	1 pc

Plywood	1 pc

Control horns 	3 pcs
plastic bolt + nut	1 + 1 pc

Rudder connecting rods	1 + 1 pc
wooden pin	1 pc

Instructions CD	1pc

Further necessary tools for assembly:

CyA glue, CyA glue accelerator, polyurethane glue, epoxy, contact glue, sharp knife

Recommended drive:

motor AXI 2212, 3s Li-pol 1300 – 1800 mAh, controller 25 A, propeller 8/6” - 9/6”

Kit assembly:

Start the assembly by cutting the grooves for carbon strip in to the wing. Cutting is done perpendicularily to the wing surface, using a sharp knife. Insert the carbon strip in to the groove and fix by thin liquid CyA glue. Stick together both halves of the wing. Apply polyurethane glue to inner surface and CyA glue to the wing circumference. Cut off the middle part of ailerons and bevel (cant) the center part. Cut off the opening for aileron servo. Make grooves in to ailerons and glue-in the levers. Use polyurethane glue. Make the ailerons rods by forming the steel wire.

Make the opening for bowden in the rear part of the body. Paste the elevator bowden in to the opening. Paste together lower part of the body with the opening. Paste well together front and rear part of the body. For pasting use CyA glue in combination with polyurethane glue.

Make the openings for elevator servo in the body cavity. Openings shall be tight. Cut the notch for ailerons’ rods in the body sidewalls.

Form the engine bedding considering on the engine type. Paste the engine bedding in to the front part of the body, using epoxy glue.  Do not forget the cooling openings. Paste complete assembly on the front part of the body.

Cut the opening for carbon strip in the middle part of the elevator. Paste the tape in to the groove using CyA glue. Form the connecting rod for the elevator (elevator junction) from steel wire and paste it inside. Paste the elevator and rudder in to the body. Pay attention to the perpendicularity of both elements. Paste the control lever in to the cuttings, using polyurethane glue.

Paste the plastic foil frame to the cabin semi-product. Paste the cabin to the body by contact glue.

In the end, check the position of the centre of gravity. In case heavier motor is mounted, make weight balancing in the rear part. Set rudder deflection to 30o at the beginning. It is recommended to make first test flights during windless weather.

Always fly in such a way to avoid injury to yourself as well as to your surroundings.

I wish you many happy hours during flying.

Libor Masik

Koberice

Czech Republic

www.lm-model.cz

# Text boxes

AC motor

elevator rod

accumulator

elevator servo

aileron servo

motor mounting 1

receiver

controller

st. kolík

C.G. (80 mm)

Notch in the body for aileron rod.

Paste part (2)

Paste part (3)

Drill the holes and paste the elevator junction

Paste the plastic foil frame to the cabin. Paste the cabin by  contact glue.

Paste pin

1

2

3

4

Cut out

Paste wing

plywood

Straight flat cutting

Paste-in part (4)

Paste the lever in to the notch.

Cut out space for servo

Rod - steel wires

Drill the opening for bowden of elevator

elevator rod

paste

Make holes in the plywood (1) according to engine

Plastic nut

430 mm

80 mm

Groove for carbon strip

270 mm

25 mm

Groove for carbon strip

pin Ø 4 mm

Aileron rod

4

Cutting by a sharp knife

Paste carbon strip by CyA glue

Cut out

paste

Elevator junction – bended wire

Paste the lever in to the notch.

receiver

elevator servo

accumulator

25 mm

2

3

4

Paste carbon strip by CyA glue

Cutting by a sharp knife

Insert carbon strip

1a

2a

1b

2b

3

4

2b

1b

3

4

1a

2a